## Slide 1: An Automotive Application of the Organic Rankine Cycle for Power Generation Using Recovered Waste Heat
Glenn Clapp
Masters project collaboration between
Grand Valley State University & GHSP

## Slide 2: Outline
Waste heat recovery
  Sources
  Recovery techniques
  Technical hurdles
Thermodynamic cycles
  Rankine cycle
  Organic Rankine cycle
  Kalina cycle
Automotive application
  Special design considerations
  Heat sources
Iterative design
  Cycle parameters
  Design space
  Mathematical modelling
  Optimization
Results
  Design specifications
  Assumptions
  Discussion
  Conclusion

## Slide 3: Outline
Waste heat recovery
  Sources
  Recovery techniques
  Technical hurdles
Thermodynamic cycles
  Rankine cycle
  Organic Rankine cycle
  Kalina cycle
Automotive application
  Special design considerations
  Heat sources
Iterative design
  Cycle parameters
  Design space
  Mathematical modelling
  Optimization
Results
  Design specifications
  Assumptions
  Discussion
  Conclusion

## Slide 4: Waste heat recovery source
This diagram shows a common breakdown of waste heat from an engine. Note that less than half of the power originally contained in the fuel produces useful work.
Automotive applications typically convert even lower percentages of power from the energy in fuel into useful work.

## Slide 5: Waste heat recovery source
The remaining energy fractions are considered waste heat. The energy from the fuel is converted into heat which is managed by vehicle systems, or escapes into the vehicle’s environment.
It is the goal of this project to harness this waste heat energy to increase the percentage of energy from fuel that does useful work.

## Slide 6: Outline
Waste heat recovery
  Sources
  Recovery techniques
  Technical hurdles
Thermodynamic cycles
  Rankine cycle
  Organic Rankine cycle
  Kalina cycle
Automotive application
  Special design considerations
  Heat sources
Iterative design
  Cycle parameters
  Design space
  Mathematical modelling
  Optimization
Results
  Design specifications
  Assumptions
  Discussion
  Conclusion

## Slide 7: Waste heat recovery techniques
Cogeneration
Kinetic energy recovery
Electricity generation

## Slide 8: Waste heat recovery techniques
Cogeneration:
Cogeneration is also referred to a combined heat and power (CHP). In a process that meets this description, electricity and useful heat are generated at the same time.
This is the most efficient and technically simple method of harvesting waste heat. The process is simply designed so that the heat generated while generating power is directly useful for some other process on site. It is essentially no longer waste.

## Slide 9: Waste heat recovery techniques
Kinetic energy recovery:
One example of kinetic energy recovery is that of the “turbocharger” which is driven by the exhaust gases from the engine to force extra compressed air into the combustion chamber and improve engine efficiency.

## Slide 10: Waste heat recovery techniques
Electricity generation:
Electricity generation is the least efficient form of waste heat recovery. Most techniques involve the use of waste heat to generate steam or some other vapor, which drives a turbine or similar device which actuates an electric generator.
This type of waste heat recovery is the subject of this project.

## Slide 11: Outline
Waste heat recovery
  Sources
  Recovery techniques
  Technical hurdles
Thermodynamic cycles
  Rankine cycle
  Organic Rankine cycle
  Kalina cycle
Automotive application
  Special design considerations
  Heat sources
Iterative design
  Cycle parameters
  Design space
  Mathematical modelling
  Optimization
Results
  Design specifications
  Assumptions
  Discussion
  Conclusion

## Slide 12: Technical hurdles
Temperature of waste heat
Heat quality
Collection
Fouling
Technical complexity
Diminishing returns

## Slide 13: Outline
Waste heat recovery
  Sources
  Recovery techniques
  Technical hurdles
Thermodynamic cycles
  Rankine cycle
  Organic Rankine cycle
  Kalina cycle
Automotive application
  Special design considerations
  Heat sources
Iterative design
  Cycle parameters
  Design space
  Mathematical modelling
  Optimization
Results
  Design specifications
  Assumptions
  Discussion
  Conclusion

## Slide 14: Traditional Rankine cycle
Process 1 -> 2: The working fluid is pumped from low to high pressure in the liquid state.
Process 2 -> 3: The high-pressure working fluid is heated at a constant pressure to a saturated vapor.
Process 3 -> 4: The saturated vapor expands through a turbine. Temperature and pressure decrease.
Process 4 -> 1: The wet vapor condenses into a saturated liquid at a constant pressure

## Slide 15: Outline
Waste heat recovery
  Sources
  Recovery techniques
  Technical hurdles
Thermodynamic cycles
  Rankine cycle
  Organic Rankine cycle
  Kalina cycle
Automotive application
  Special design considerations
  Heat sources
Iterative design
  Cycle parameters
  Design space
  Mathematical modelling
  Optimization
Results
  Design specifications
  Assumptions
  Discussion
  Conclusion

## Slide 16: Organic Rankine cycle
The organic Rankine cycle is the same exact cycle in practice. The only difference is the working fluid. In the organic Rankine cycle working fluids with low phase transition temperatures, such as hydrocarbons and refrigerants, are chose. The are “organic molecules.”
Organic molecules are those usually found in living systems. Organic molecules are usually composed of carbon atoms in rings or long chains, to which are attached other atoms of such elements as hydrogen, oxygen, and nitrogen.

## Slide 17: Outline
Waste heat recovery
  Sources
  Recovery techniques
  Technical hurdles
Thermodynamic cycles
  Rankine cycle
  Organic Rankine cycle
  Kalina cycle
Automotive application
  Special design considerations
  Heat sources
Iterative design
  Cycle parameters
  Design space
  Mathematical modelling
  Optimization
Results
  Design specifications
  Assumptions
  Discussion
  Conclusion

## Slide 18: The Kalina cycle
The Kalina cycle is also a Rankine cycle. The innovation of the Kalina cycle is its use of a non-azeotropic working fluid. That is, the working fluid is a composition of multiple fluids such that it has a variable phase transition temperature. This allows the cycle to closely match the appropriate phase transition temperature to the heat source available.
The Kalina cycle is much more technically complex in implementation than the organic Rankine cycle, and requires higher working temperatures which make it less suitable for an automotive application.

## Slide 19: Outline
Waste heat recovery
  Sources
  Recovery techniques
  Technical hurdles
Thermodynamic cycles
  Rankine cycle
  Organic Rankine cycle
  Kalina cycle
Automotive application
  Special design considerations
  Heat sources
Iterative design
  Cycle parameters
  Design space
  Mathematical modelling
  Optimization
Results
  Design specifications
  Assumptions
  Discussion
  Conclusion

## Slide 20: Automotive application design considerations
Limited package space
Narrow range of waste heat temperature availability (~100oC)

## Slide 21: Outline
Waste heat recovery
  Sources
  Recovery techniques
  Technical hurdles
Thermodynamic cycles
  Rankine cycle
  Organic Rankine cycle
  Kalina cycle
Automotive application
  Special design considerations
  Heat sources
Iterative design
  Cycle parameters
  Design space
  Mathematical modelling
  Optimization
Results
  Design specifications
  Assumptions
  Discussion
  Conclusion

## Slide 22: Automotive heat sources
Exhaust stream
Coolant
The exhaust stream has a lot of drawbacks that the coolant stream doesn’t have. The exhaust temperature must remain high for certain emission control reactions (catalytic converter) , there are a lot of volatile compounds in the exhaust stream that would degrade heat exchanger performance, and raising the pressure of the exhaust stream by restricting its flow would affect the performance of the engine negatively.
In contrast, the advantages of harnessing heat from the coolant stream are that the temperature of the fluid is relatively consistent, it’s the expected heat sink for the vehicle system in the first place, and it is already circulating under the power of the vehicle pump and so reduces the number of additional components in the proposed system.

## Slide 23: Outline
Waste heat recovery
  Sources
  Recovery techniques
  Technical hurdles
Thermodynamic cycles
  Rankine cycle
  Organic Rankine cycle
  Kalina cycle
Automotive application
  Special design considerations
  Heat sources
Iterative design
  Cycle parameters
  Design space
  Mathematical modelling
  Optimization
Results
  Design specifications
  Assumptions
  Discussion
  Conclusion

## Slide 24: Cycle parameters
Working fluid
Mass flow rate
Working pressure & temperature of boiler
Working pressure & temperature of condenser
Surface area of heat exchangers
Turbine stages
Turbine blade size/shape/angle

## Slide 25: Outline
Waste heat recovery
  Sources
  Recovery techniques
  Technical hurdles
Thermodynamic cycles
  Rankine cycle
  Organic Rankine cycle
  Kalina cycle
Automotive application
  Special design considerations
  Heat sources
Iterative design
  Cycle parameters
  Design space
  Mathematical modelling
  Optimization
Results
  Design specifications
  Assumptions
  Discussion
  Conclusion

## Slide 26: Working pressure and temperature preliminary results

## Slide 27: Outline
Waste heat recovery
  Sources
  Recovery techniques
  Technical hurdles
Thermodynamic cycles
  Rankine cycle
  Organic Rankine cycle
  Kalina cycle
Automotive application
  Special design considerations
  Heat sources
Iterative design
  Cycle parameters
  Design space
  Mathematical modelling
  Optimization
Results
  Design specifications
  Assumptions
  Discussion
  Conclusion

## Slide 28: Proposed modelling

## Slide 29: Outline
Waste heat recovery
  Sources
  Recovery techniques
  Technical hurdles
Thermodynamic cycles
  Rankine cycle
  Organic Rankine cycle
  Kalina cycle
Automotive application
  Special design considerations
  Heat sources
Iterative design
  Cycle parameters
  Design space
  Mathematical modelling
  Optimization
Results
  Design specifications
  Assumptions
  Discussion
  Conclusion

## Slide 30: Outline
Waste heat recovery
  Sources
  Recovery techniques
  Technical hurdles
Thermodynamic cycles
  Rankine cycle
  Organic Rankine cycle
  Kalina cycle
Automotive application
  Special design considerations
  Heat sources
Iterative design
  Cycle parameters
  Design space
  Mathematical modelling
  Optimization
Results
  Design specifications
  Assumptions
  Discussion
  Conclusion

## Slide 31: Design specifications
The results of optimizing the mathematical model will be used to inform the design specifications for prototyping and iterative design

## Slide 32: Outline
Waste heat recovery
  Sources
  Recovery techniques
  Technical hurdles
Thermodynamic cycles
  Rankine cycle
  Organic Rankine cycle
  Kalina cycle
Automotive application
  Special design considerations
  Heat sources
Iterative design
  Cycle parameters
  Design space
  Mathematical modelling
  Optimization
Results
  Design specifications
  Assumptions
  Discussion
  Conclusion

## Slide 34: Outline
Waste heat recovery
  Sources
  Recovery techniques
  Technical hurdles
Thermodynamic cycles
  Rankine cycle
  Organic Rankine cycle
  Kalina cycle
Automotive application
  Special design considerations
  Heat sources
Iterative design
  Cycle parameters
  Design space
  Mathematical modelling
  Optimization
Results
  Design specifications
  Assumptions
  Discussion
  Conclusion

## Slide 36: Outline
Waste heat recovery
  Sources
  Recovery techniques
  Technical hurdles
Thermodynamic cycles
  Rankine cycle
  Organic Rankine cycle
  Kalina cycle
Automotive application
  Special design considerations
  Heat sources
Iterative design
  Cycle parameters
  Design space
  Mathematical modelling
  Optimization
Results
  Design specifications
  Assumptions
  Discussion
  Conclusion